## Slide 1: COA Lab Project (2016-17) The LNMIIT, Jaipur
SMART JACKET
Himanshi Swaroop (15ucs052)
Harshali Jain (15ucs047)
Sonal Jain (15ucs054)

## Slide 2: Introduction
Protects smartphone users from losing their phones
Anxiety about keeping your phone charged all the time.
Inconvenience of having to take out your phone from pockets or bags to change songs.
Helps reduce stress(in the form sleep shade)
Location tracker inbuilt
Inconvenience of having to take out your phone from pockets or bags to call someone
Thermoregulation
Distractions from important matters due to constant messages and calls
So here is the solution for all above problems that is
SMART JACKET!!

## Slide 3: Functions
1.Password: Jacket can be used only when password is correct. The password given by the user is passed as a integer(0-7) which is verified by the function.
Pass R00
2.Music:Song is taken from register. This function searches for passed song and plays it if found. Contains mnemonic MOV which moves favourite song no. to register(MOV register,integer ).
Music R00
3.Charge:It is responsible for charging the phone.If battery is below 40%,it starts charging the phone and switch on the LED light.
Charge R01
4.Sleep Shade: When the corresponding button is pressed then the shades slides down.
Sleepshade
5.Connect Call: To whom we have to call is passed as into register and if this name is available in the contact list it calls the person.
Connect R01

## Slide 4
6.Loss Prevention: It alerts when the phone is lost and finds it if it is available in any direction in a particular range
Loss
7.Notification: It notifies for call or sms on mobile.
Notify R01 (bit tells whether it is sms or a call)
8.Distance-Time Finder: It gives the distance and time taken between source and destination
Distancetime R01,R02
9.Thermoregulation: It regulates the temperature according to the users requirement(hot or cold)
Temp R00 (bit 0:hot and 1:cold)
10. JMP : It compares the result of previous instruction with 0 and jumps to a particular label.
  JMP R01, Label

## Slide 5: Memory Model
Aligned Memory Model
RAM Sizes-
  Storing Instruction- 12x8
  Storing Data- 8x8
Little Endian
Byte Addressable

## Slide 6: Registers
General Purpose Registers– 4
R00 – R03
Special Purpose Registers –
Program Counter, Instruction Register, Zero Flag, Negative Flag

## Slide 7: Instruction Format
2 Address Instructions –
1 Address Instructions –
0 Address Instructions –
OPCODE | OPERAND 1 | OPERAND 2
2 bits 3 bits 3 bits
OPCODE | OPERAND 1
5 bits 3 bits
OPCODE
8 bits

## Slide 8: Instruction Design
Two Addressable
  Distancetime- 00 xxx yyy
  Mov- 01 xxx yyy
  JMP – 10 xxx yyy
    (Escape Code – 11)
One Addressable
  Charge- 11 000 xxx
  Music- 11 001 xxx
  Temp- 11 010 xxx
  Connect- 11 011 xxx
  Pass- 11 100 xxx
  Notify- 11 101 xxx
  Decrement- 11 110 xxx
    (Escape Code – 111)

## Slide 9: Continued…
Zero Addressable
  Sleepshade- 11 111 000
  Loss- 11 111 001
  HALT- 11 111 010

## Slide 10: Instruction Types
Data Transfer - MOV
Dyadic Operations -Distancetime
Monodic Operations - Charge, Music, Temp, Callconnect, Decrement, Pass, Notify
Procedure Call/Compare Functions -JMP, Pass
Arithmetic - Temp, Charge, Distancetime

## Slide 11: Data Types
Numeric –
  Integer

## Slide 12: Addressing Modes
Direct Mode
Immediate Mode

## Slide 13: Flow of Control Handling
JMP : It compares the result of previous instruction with the provided value and jumps to a particular label.
  JMP <Register>,<Label>
HALT: Halts the procedure containing it.
    HALT

## Slide 14
DATA PATH-SINGLE BUS ARCHITECTURE
Select lines | Select 0 | Select 1
Select 4 | 0 | 0
Select 7 | 0 | 1
Select 1 | 1 | 0
Select Y | 1 | 1
Multiplexer

## Slide 15
ALU DESIGN
Operation | S0 | S1
Add | 0 | 0
Subtract | 0 | 1
Multiply | 1 | 0
Sqrt | 1 | 1
ALU control Signals

## Slide 16
FULL ADDER/SUBTRACTOR

## Slide 17
HARDWIRED CONTROL UNIT

## Slide 18
Micro-Instructions
PASS R00
1-Pcout,MARin,READ,SELECT4,ADD,Zin
2-Zout,PCin,Yin,WMFC
3-MDRout,IRin
4-R00out,Select4,sub,Zin
5-if ZF=1 then OUT
6-end
MOV R02 2
1-Pcout,MARin,READ,SELECT4,ADD,Zin
2-Zout,PCin,Yin,WMFC
3-MDRout,IRin
4-DCout,R02in
5-END
DEC R02
1-Pcout,MARin,READ,SELECT4,ADD,Zin
2-Zout,PCin,Yin,WMFC
3-MDRout,IRin
4-R02out,SELECT1,sub,Zin
5-Zout,R02in
6-END
JMP R02 LABEL1
1-Pcout,MARin,READ,SELECT4,ADD,Zin
2-Zout,PCin,Yin,WMFC
3-MDRout,IRin
4-Offset-field-ofIRout,SELECTY,ADD,Zin,If ZF=1 then End
5-Zout,Pcin,END

## Slide 19
DIS R01,R02
1-Pcout,MARin,READ,SELECT4,ADD,Zin
2-Zout,PCin,Yin,WMFC
3-MDRout,IRin
4-R01out,Yin
5-SELECTY,MUL,Zin
6-Zout,R01in
7-R02out,Yin
8-SELECTY,MUL,Zin
9-Zout,R02in
10-R01out,Yin
11-R02out,SELECTY,add,Zin
12-Zout,SQRT,Zin
13-Zout,R01in
14-END
CRGE R00
1-Pcout,MARin,READ,SELECT4,ADD,Zin
2-Zout,PCin,Yin,WMFC
3-MDRout,IRin
4-R00out,SELECT4,sub,Zin
5-if NF=1 then OUT
6-END
MUSI R01
1-Pcout,MARin,READ,SELECT4,ADD,Zin
2-Zout,PCin,Yin,WMFC
3-MDRout,IRin
4-R01out,SELECT7,sub,Zin
5-if NF=1 then OUT
6-END
CONN R02
1-Pcout,MARin,READ,SELECT4,ADD,Zin
2-Zout,PCin,Yin,WMFC
3-MDRout,IRin
4-R02out,SELECT7,sub,Zin
5-if NF=1 then OUT
6-END
NOTIFY R00
1-Pcout,MARin,READ,SELECT4,ADD,Zin
2-Zout,PCin,Yin,WMFC
3-MDRout,IRin
4-R00out,Zin,if ZF=1 then OUT
5-END

## Slide 20
TEMP R01
1-Pcout,MARin,READ,SELECT4,ADD,Zin
2-Zout,PCin,Yin,WMFC
3-MDRout,IRin
4-IOout,SELECT4
5-if ZF=1 then sub,Zin else add,Zin
6-END
HALT
1-Pcout,MARin,READ,SELECT4,ADD,Zin
2-Zout,PCin,Yin,WMFC
3-MDRout,IRin
4-HLT

## Slide 21
HARDWIRED CONTROL SIGNALS
1.
2.
3.
There are 30 control signals:
Pcin, Pcout, Read, MARin, Select Y,WMFC, MARin,DCout,IRin,IOout,SelectY,Select7,Select1,Mult,Yin,R00in,R00out,R01in, R01out,R02in,END,Zin,ADD,SQRT,HALT,R02out,Zout,SUB,OUT.

## Slide 22
4.
5.

## Slide 23
7.

## Slide 24
8.
9.
10.
11.
9.
11.

## Slide 25
12.
13.
14.
15.

## Slide 26
16.Yin
17.
18.
19.

## Slide 27
20.
21.

## Slide 28
22.

## Slide 29
23.

## Slide 30
HALT
24.
25.
26.

## Slide 31
27.

## Slide 32
28.

## Slide 33
29.

## Slide 34
OUT
30.

## Slide 35: Thank You
THE END